Physical Disabilities (Missing or Non-Functional Body Parts), Their Effects on Driving and Suggested Driving Aids

| Disability | Effects on Driving | Suggested Driving Aids |
| --- | --- | --- |
| Left Leg Missing or Non-Functional | • Inability to use left foot on dimmer switch and foot-operated parking brake • Possible inability to maintain body balance • Inability to use clutch • Possible interference of leg or foot with accelerator or brake | • Hand-operated dimmer switch and parking brake (or center console parking brake) • Shoulder or chest strap and/or arm rests if sitting balance is impaired • Automatic transmission • Quick release accelerator and brake pedal block |
| Right Leg Missing or Non-Functional | • Inability to use standard accelerator • Possible inability to maintain body balance • Awkwardness in using left foot dimmer switch (because left foot occupied w/brake and accelerator) • Inability to use clutch • Possible interference of leg or foot with accelerator or brake | • Left-foot accelerator with accelerator pedal block • Shoulder or chest straps and/ or arm rests if sitting balance is impaired • Hand-operated dimmer switch • Automatic transmission • Quick release accelerator and brake pedal block |
| Both Legs Missing or Non-Functional | • Inability to use brake and accelerator • Inability to use dimmer switch or foot-operated parking brake • Possible difficulty maintaining body balance • Possible interference of leg or foot with accelerator or brake • Possible difficulty entering/exiting the car and loading mobility device(s) | • Hand-operated brake and accelerator, necessitating automatic transmission • Hand-operated dimmer switch and parking brake • Special seat structure, cushions, arm rests, or chest/shoulder strap if sitting balance or trunk control is impaired • Quick release accelerator and brake pedal block • A grab bar, strap, transfer board or swivel seat may be helpful to enter and exit the vehicle |
| Left Arm Below Elbow Missing or Non-Functional | • Difficulty performing timely and smooth hand-over-hand steering maneuvers • Inability to shift gears while steering • Difficulty grasping and pulling left-hand dash controls • Inability to use turn signal and other controls mounted on lever (wipers, cruise control) | • Power steering and spinner knob attached to steering wheel, mounted at 2 or 5 o'clock position, for the non-involved hand • Automatic transmission • Rings attached to left-hand dash controls • Right side turn signal modification or remote/electronic secondary controls |

| Disability | Effects on Driving | Suggested Driving Aids |
| --- | --- | --- |
| Right Arm Below Elbow Amputation or Non-Functional | • Difficulty performing hand-over-hand steering maneuvers • Inability to shift gears while steering • Difficulty grasping and pulling right-hand dash controls | • Power steering and spinner knob attached to steering wheel, mounted at 10 or 7 o'clock position, for the non-involved hand • Rings or extensions attached to right-hand dash controls • Although a driver with a right-hand hook should be able to operate either a standard or an automatic shift lever, automatic transmission is easier Presetting auxiliary controls prior to driving Key extension lever to assist with operating the ignition |
| Both Arms Below Elbow Amputation or Non-Functional | • Inability to grasp and turn regular steering wheel • Difficulty grasping and pulling dashboard controls • Difficulty grasping and pulling or turning other small devices or control in the car (door locks and handles, window cranks, ashtray, glove compartment, radio knobs, etc.) | With a Prosthesis: • Driving ring or steering knob attached to the steering wheel, on the side of the dominant arm • Rings attached to the dashboard controls • Ring attachments for any small device or controls difficult to operate; electric door locks and power windows No Prothesis: • The driver should be able to maneuver the steering wheel using two arms; if not, an extended/telescopic steering column is recommended • Dashboard extensions • Power door locks and power windows; keyless ignition |
| Left Arm Above Elbow Amputation or Non-Functional | • Inability to perform smooth and timely hand-over-hand steering maneuvers • Inability to use left-hand turn signal • Difficulty reaching left-hand dashboard controls • Difficulty releasing left-hand parking brake • Inability to shift gears on standard transmission while right arm is occupied • Difficulty activating horn while right hand is occupied | • Steering knob or other steering aid mounted on the right • Right-hand extension turn signal lever or electrical signal • Right-hand extensions on left-hand dashboard controls, or dashboard models with right-hand controls • Parking brake release adapted for use by the left foot or the right hand • Automatic transmission • Horn ring that can be reached without letting go of the steering knob |
| Right Arm Above Elbow Amputation or Non-Functional | • Inability to perform smooth and timely hand-over-hand steering maneuvers • Difficulty reaching right-hand dashboard controls • Possible difficulty turning ignition key • Inability to use right-hand gear selector • Inability to use clutch | • Steering knob or other device mounted on the left • Left-hand extensions for dashboard controls and/or dashboard model with some left-hand controls • Ignition key reachable with the left hand while parked, or adapted for the left hand • Left-hand extension of gear shift lever • Automatic transmission |
| Disability | Effects on Driving | Suggested Driving Aids |
| Both Arms Above Elbow Amputation or Non-Functional | • Inability to use conventional steering wheel • Inability to operate standard transmission • Inability to operate turn signal, ignition key, gear selector, dash controls, horn, parking brake release | • Foot steering controls: a metal boot mounted on a circular disk in the floor-board, by the left foot • Automatic transmission • Gear selector on the floor, by the right foot; horn and turn signal on the floor, or remote controls for knee operation; ignition, lights, windshield wipers, and emergency brake underneath and behind instrument panel |
| Lack of Manual Dexterity | • Limited ability to grasp and turn steering wheel • Limited ability to grasp and operate ignition and dashboard controls • Difficulty releasing hand-operated parking brake | • Tri-post, "V," of cuff-type steering wheel spinner • Ignition key holder; rings or other adaptations on dashboard controls • Foot-operated parking brake, or extension loop on the parking brake handle |
| Both Arms and Both Legs Disabled (Quadriplegia) Low Level Quadriplegia - Able to Transfer Into Car | • Inability to use brake, accelerator, dimmer switch, foot-operated parking brake, and clutch • Limited ability to grasp and turn steering wheel • Limited ability to maintain body balance • Possible limited ability to see full field of traffic • Difficulty entering car and storing wheelchair • Possible fatigue • Difficulty using dashboard controls, ignition key, and seat belt fixture | • Hand-operated brake, accelerator, dimmer switch (may be combined with horn switch); extension and loop on parking brake; automatic transmission and parking brake • "Quad" steering device ("V" shaped grip, semicircle, steering pin, or tripost, as necessary); wrist cuff; wrist splint or elbow support • Chest harness safety belt, arm rests, cushions • Side view mirrors and full-range rear-view mirrors if neck or trunk rotation is limited • Two-door car; grab bar or strap; transfer board; wheelchair hoist • Instruction in avoiding and dealing with fatigue; driving lessons planned with awareness of student's stamina range • Ignition key holder and adaptations of seat belt fixtures and other small devices |
| Both Arms and Both Legs Disabled (Quadriplegia) High Level Quadriplegia – Unable to Transfer into Car and Must Drive Van from Wheel Chair | • Inability to use brake, accelerator, dimmer switch, foot-operated parking brake, and clutch • Limited ability to grasp and turn steering wheel • Limited ability to maintain body balance • Possible limited ability to see full field of traffic • Difficulty entering car and storing | • Quad hand controls, which may have dimmer-plus-horn and signals incorporated or servo controls. The dimmer switch can be controlled by the elbow; electric parking brake; automatic transmission • "Quad" steering device, if necessary; adjustable height, position, and diameter of steering wheel, as well as adjustable steering column position; "low" or "zero" effort steering with emergency back up • Wheelchair restraint-a safety locking device to prevent the wheelchair from moving; passenger restraint could include a lap belt, chest harness, lateral supports attached to the wheelchair, and a special quad seat belt |

| Disability | Effects on Driving | Suggested Driving Aids |
| --- | --- | --- |
| Both Arms and Both Legs Disabled (Quadriplegia) High Level -cont. | wheelchair • Possible fatigue • Difficulty using dashboard controls, ignition key, and seat belt fixture | • Power pan or wheel channels; special mirrors • Automatic wheelchair lift; wheelchair restraint • Instruction in avoiding and dealing with fatigue; air conditioning, cruise control, easy/zero effort controls • Keyless ignition, or ignition relocated to an accessible area; dashboard controls converted to a special quad console with toggle switches and/or dashboard control extensions |
| Lack of Range of Motion – Upper Extremities | • Limited ability to turn steering wheel • Possible difficulty operating dashboard controls, gear shift, ignition key, and parking brake release • Limited ability to see the full field of traffic | • Extension of steering wheel column and small wheel with spinner knob; or, foot-operated steering if limitation is severe • Extensions or adaptations of dashboard controls, gear shift lever, turn switch and ignition switch, and foot-operated parking brake • Panoramic rear and side view mirrors |
| Lack of Range of Motion - Hips | • Difficulty using brake and accelerator • Difficulty using dimmer switch and parking brake • Difficulty using clutch • Possible difficulty turning to watch rear view while backing up • Possible difficulty entering and leaving car | • Hand-operated brake and accelerator • Hand-operated dimmer switch and parking brake • Automatic transmission • Panoramic rear view mirror • Grab bar or strap (swivel seats are also helpful); power seats |
| Lack of Body Balance | • Danger of falling to one side in turns or sudden motions | • Specially constructed seat for balance; arm rests; cushions and or shoulder or chest safety belts |
| Poor Muscle Control, e.g., tremors, ataxia, dystonia, etc. | • Difficulty controlling steering wheel • Uncontrolled involuntary movement, or spasms of rigidity may present too great a danger for driving | • Tri-post, "V," or cuff-type steering wheel spinner • Persons suffering from uncontrolled muscle activity that is potentially dangerous for driving should consult a driver rehabilitation specialist before going on the road. If spasms occur in the legs only and hand controls are used, a brake/accelerator block can be used |
| Lack of range of Motion in Neck or Trunk | Difficulty performing left-right-left traffic checks prior to proceeding through intersections Difficulty performing shoulder checks to check blind spots prior to merging and changing lanes Difficulty backing a vehicle Difficulty checking traffic at intersections with skewed geometry | Specially designed panoramic mirrors mounted on outside mirrors Specially designed panoramic mirror attached to rearview mirror Individually placed panoramic mirrors installed on dash or A Frame to effectively observe traffic to all sides of vehicle Multi-panel wide angle mirrors replacing rearview mirror Electronic back up sensors to alert driver when close to objects, e.g., curbs and objects behind when backing Video cameras with in-vehicle monitors to allow driver to be aware of traffic around vehicle |